## Slide 1: Architectural CAD I – IM230
Vocabulary

## Slide 2: GROUP 3
Vocabulary

## Slide 3
ACCORDION PARTITION
A fabric-faced partition which is hung from an overhead track and folds back like the bellows of an accordion
BI-FOLDING DOOR
A door having two pairs of leaves that are hinged together, with one side pivoted to the jamb, while the other side slides open and closed in the overhead track

## Slide 4
AWNING WINDOW
A window that the top horizontal sash is top-hinged and the bottom sash swings inward or outward
CASEMENT WINDOW
A window that’s side sash swings open along the entire length

## Slide 5
CASEWORK
The aggregate assembled parts (including framework, finish, doors, drawers, etc.) which make up a case or cabinet
CASING
The exposed trim molding, framing, or lining around a door or window

## Slide 6
CHAIR RAIL
A horizontal strip usually of wood, affixed to the wall at a height which prevents the backs of chairs from damaging the wall surface
CROWN MOLDING
Any molding forming the crowning or finishing member of a structure or along a ceiling

## Slide 7
CLERESTORY
An upper zone of wall pierced with windows that admit light into the room
DOUBLE GLAZING
Two panes of glass, usually parallel, with an air space between; used to provide increased thermal and/or sound insulation

## Slide 8
DEADBOLT
A type of door lock which is operated by the door key or turning piece
DOOR CLOSER
A device, containing a spring, for controlling the speed to automatically close a door

## Slide 9
DOUBLE HUNG WINDOW
A window having two vertically sliding sashes, each closing a different part of the window
GLAZING
The glass surface of a glazed opening

## Slide 10
FINISH HARDWARE
Hardware, such as hinges, locks, knobs, etc., that has a finished appearance as well as a function, which are usually used with doors, windows, and cabinets
HINGE
A movable joint used to attach, support, and turn a door about a pivot

## Slide 11
FRENCH DOORS
A door having a top and bottom rail and stiles, which has glass panes throughout its entire length
GASKET/WEATHER STRIPING
A continuous strip of resilient material attached to a door or door frame to provide a tight seal between the door and frame, it also provide a barrier from the weather, light, and sound

## Slide 12
HOLLOW CORE DOOR
A flush door of hollow-core construction
HOLLOW METAL DOOR
A flush metal door, fabricated of sheet steel and reinforced by light metal channels; sometimes filled with a light filler material

## Slide 13
JAMB
A vertical member at either side of a door or window frame
KICKPLATE
A protective plate applied on the lower rail of a door to prevent marring

## Slide 14
LATCH
A simple fastening device having latch bolt, but not a dead bolt, contains no provisions for locking with a key; usually operable from both sides
LOCKSET
A complete lock system including the basic locking mechanism and all the accessories, such as knobs, levers, plates, etc

## Slide 15
MILLWORK
Ready-made products which are manufactured at a wood-planning mill or woodworking plant: moldings, doors, door frames, window sashes, stair work, cabinets, etc
MULLION
A vertical member separating (and often supporting) window, door, or panels set in series

## Slide 16
OVERHEAD DOOR
A door that either swings up or rolls up, which when open, assumes a horizontal position above the door opening
PANEL DOOR
A door having stiles, rails and sometimes mutins which form one or more frames around recessed panels

## Slide 17
POCKET DOOR
A door that recesses into a wall
PREHUNG DOOR
An assembly consisting of a door on its frame, together with all necessary hardware and trim, ready for installation

## Slide 18
PUSH BAR/PANIC
A heavy bar fixed across a glazed door used to open or closed the door, while providing protection for the glass
SASH
Any framework of a window

## Slide 19
SKYLIGHT
An opening which is glazed with a transparent or translucent material that is located in the roof
TRANSOM
A horizontal bar of wood or stone across a window or door. Also, a window located above a door

## Slide 20
SOLID-CORE DOOR
A door having a core of solid wood or mineral composition
SPANDREL GLASS
An opaque glass used in windows and curtain walls to conceal internal construction

## Slide 21
TEMPERED GLASS
Glass having two or four times the strength of ordinary glass as a result of being prestressed by heating and then suddenly quenched
TRANSLUCENT
A material that transmits light but diffuses is sufficiently so that an image cannot be seen through the material clearly

## Slide 22
THRESHOLD
A strip fastened to the floor beneath a door to cover the joint where two types of flooring material meet; may provide weather protection at exterior doors
TOE KICK
A space provided, typically in cabinetry, for toe space

## Slide 23
TRIM
The visible woodwork or moldings of a room, such as the baseboards, chair rail, crown molding, door and window casing, etc
WAINSCOT
A decorative or protective facing applied to the lower portion of an interior partition or wall